## Slide 1: Avionics
Led by Morgan Novak

## Slide 2: Objectives:
Receive telemetry data from the rocket during launch
Stream video of rocket
Display data in an interesting way
Optional: Play sound from speakers at lift off and touchdown
Use LoRa to send sensor data from rocket to ground.
Sensors:
Barometer*
Altimeter*
Temperature*
Accelerometer
*all in one chip
Use FPV Drone Camera/Transmitter Package to send video from rocket to ground.
Backup: Firefly Camera that saves to SD card
Display data from sensors and live video on monitor.
Port sensor data into launch control box.
Host website on Groundpi.
Notes: Morgan

## Slide 3
*Monitor not shown
Notes: Morgan

## Slide 4: Sensors RockPi
Barometer+Temperature+Altitude
Adafruit BMP280
SPI or I2C
Altitude based on pressure @ sea level (<10m)
Accelerometer
Adafruit MMA8451
I2C
Auto-tilt orientation detection
14 bit ADC
5V
SCL
GND
SDA
3.3V
SCL
SDA
GND
GND
Notes: Morgan

## Slide 5: LoRa RockPi + GroundPi
Used to send sensor data from RockPi to GroundPi
  SPI
  Sends/receives packets over 2km
Range Testing on B14 Antenna Range
  ~1,874 ft
5V
Radio GPIO
Antenna
GND
G0
CLK
MISO
MOSI
CS
RST
Notes: Kathryn

## Slide 6: FPV Camera + Transmitter RockPi
600TVL 1/4 1.8mm CMOS FPV 170 Degree Wide Angle Camera
  PAL/NTSC
  3.7-5V
Eachine VTX02 Super Mini 5.8G 40CH 200mW FPV Transmitter
  No audio
  3.3V
Camera Transmitter
Transmitter Pi
  POWER ONLY
Notes: Kolten

## Slide 7: FPV Receiver GroundPi
Eachine ROTG01 UVC OTG 5.8G 150CH Full Channel FPV Receiver
  Range: 1476.38ft
  Plugs into PC
Range: 3280.84ft
*Ranges are as advertised, did not have time to test
Notes: Kolten

## Slide 8: Displays GroundPi
Website
Hosted by Ground PC
Screen capture of live display on monitor
Launch Control Box
7-segment displays for Altitude, Barometer, Accelerometer
Notes: Elliot

## Slide 9: RockPi
Pi Zero
Notes: MDT

## Slide 10: Power
Anker Astro E1 Battery
Capacity: 5200 mAh / 19.24 Wh
Output: 5 V / 2 A
Weight: 119 g / 4.2 oz
Size: 3.8 x 1.7 x 0.9 in
Notes: MDT